## Slide 1: Switching Theory
Class-1

## Slide 2: Switches
A
B
A simple on/off switch
IF switch is closed THEN light is on
+
5V
-
IF switches A AND B AND C are closed THEN light is on
+
5V
-
A
B
C
+
5V
-
A
B
C
IF switches A OR B OR C are closed THEN light is on

## Slide 3: A Few Words About Resistors
For our purposes, we can use a very simple model of resistors:
No Connection (Open)
A
B
Good Connection (A wire)
A
B
Poor Connection (Resistor)
A
B
Consider these combinations:
+5V
A
0V
Good
None
+5V
Good wins over None
+5V
B
0V
Poor
None
+5V
Poor wins over None
+5V
C
0V
Poor
0V
Good
Good wins over Poor
+5V
0V
+5V
0V
Don’t do this!

## Slide 4: Controlling Switches
A
B
A simple on/off switch with control
Control
If Control is > 2.5V, switch is closed otherwise, switch is open.
Threshold
Note: Assume switches are always closed with higher voltage, open with lower voltage.

## Slide 5: A circuit using switches
5V
GND = 0V
Vin
Vout
Inverter
Vin
Vout
Vin switch Vout
0V open 5V
5V closed 0V
5V
GND = 0V
Vin=5
Vout=0
5V
GND = 0V
Vin=0
Vout=5

## Slide 6: Using Outputs as Inputs
VCC=5V
Vin
Vout
Vmid
Vin
Vmid
Vout
Vin Vmid Vout
0V 5V 0V
5V 0V 5V
Buffer
Vin
Vout

## Slide 7: What is the Use of a Buffer
While this may seem like a pointless thing to do, it does have practical application. Remember that gate circuits are signal amplifiers, regardless of what logic function they may perform.
A weak signal source (one that is not capable of sourcing or sinking very much current to a load) may be boosted by means of two inverters like the pair shown in the previous illustration.
The logic level is unchanged, but the full current-sourcing or -sinking capabilities of the final inverter are available to drive a load resistance if needed.

## Slide 8
Digital Buffers can be used to isolate other gates or circuits from each other or buffers can be used to drive high current loads such as transistor switches because their output drive capability is much higher than their input signal requirements. In other words buffers can be used for power amplification of a digital signal as they have what is called a high "fan-out" capability.
Buffer Fan-out Example
The Fan-out parameter of a buffer (or any digial IC) is the output driving capability or output current capability of a logic gate giving greater power amplification of the input signal. It may be necessary to connect more than just one logic gate to the output of another or to switch a high current load such as an LED, then a Buffer will allow us to do just that.
Generally the output of a logic gate is usually connected to the inputs of other gates. Each input requires a certain amount of current from the gate output to change state, so that each additional gate connection adds to the load of the gate. So the fan-out is the number of parallel loads that can be driven simultaneously by one digital buffer of logic gate. Acting as a current source a buffer can have a high fan-out rating of up to 20 gates of the same logic family.
If a digital buffer has a high fan-out rating (current source) it must also have a high "fan-in" rating (current sink) as well. However, the propagation delay of the gate deteriorates rapidly as a function of fan-in so gates with a fan-in greater than 4 should be avoided.

## Slide 9: Some more Switch Logic
VCC
VA
Vout
VB
Vout is 0V only if VA AND VB are both 5V
A
B
C
NAND gate
VA VB Vout
0V 0V 5V
0V 5V 5V 5V 0V 5V 5V 5V 0V
A
B
C
AND gate
A
B
C

## Slide 10: Even more Switch Logic
C is L if A OR B is H
NOR gate
VCC
A
C
B
L = 0V, H = 5V
A B C
L L H
L H L H L L H H L
A
B
C
A
B
C
A
B
C
OR gate

## Slide 11: Voltage-controlled Switches
In order to build circuits that implement logic, we need voltage-controlled switches
  Control input = 1  Switch is closed
  Control input = 0  Switch is open
A
B
Control
This can be accomplished with electro-mechanical relays
  Large, clunky, power-hungry
Transistors are a better way
  Tiny, efficient, fast
Source
Drain
Gate

## Slide 12: MOS Semiconductor Transistors
Silicon Bulk (p-type)
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
e-
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
e-
e-
e-
e-
e-
Source
e-
e-
e-
e-
Drain
Gate
n-type Si
n-type Si
Source Wire
Drain Wire
Gate Wire
Oxide
P-type silicon: Excess positive charges (electron holes)
N-type silicon: Excess negative charges (electrons)
Oxide: Insulator
Gate: Metal pad
In this state, current (electrons) cannot flow between source and drain – switch is OPEN

## Slide 13: MOS Semiconductor Transistors
Silicon Bulk (p-type)
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
e-
e-
e-
e-
e-
Source
e-
e-
e-
e-
Drain
Gate
n-type Si
n-type Si
Source Wire
Drain Wire
Gate Wire
Oxide
Place a positive charge on the gate wire (gate = +5V)
+5V
+
+
+
+
+
+
+
+
The gate’s positive charge attracts negatively-charged electrons
+
e-
e-
e-
e-
e-
e-
e-
e-
e-
This row of electrons forms a channel connecting the Source and Drain – Current can flow – Switch is CLOSED
e-
e-

## Slide 14: Voltage-controlled switches
Logic 1 on gate:
Source and Drain connected
Gate
Source
Drain
nMOS Transistor
Gate
Source
Drain
pMOS Transistor
Logic 0 on gate:
Source and Drain connected
Gate
Source
Drain
Gate
Source
Drain
nMOS: Good connector to GND Poor connector to +5
pMOS: Poor connector to GND Good connector to +5

## Slide 15: An nMOS Inverter
Issues
  When transistor (switch) is closed, some current goes directly from 5V to GND
    Wastes power; creates heat
5V
GND = 0V
Vin
Vout
5V
GND = 0V
Vin
Vout
Replace the switch with an NMOS transistor
  When transistor (switch) is open, current must flow through the resistor
    Wastes power; creates heat

## Slide 16: CMOS Inverter
Input is 1
Pull-up does not conduct
Pull-down conducts
Output connected to GND
Input is 0
Pull-up conducts
Pull-down does not conduct
Output connected to Vdd
5V = 1
GND = 0
Pull-up pMOS transistor
Pull-down nMOS transistor
Current
Current
Note that there is never current leakage…
GND
+5V
A
Z
GND
+5V
A
Z
GND
+5V
A
Z
1
0

## Slide 17: CMOS NAND Gate
A = 1, B = 1
Output is GND=0
A = 0, B = 1 or A=1, B=0
Output is Vdd=1
Pull-up pMOS Network
Pull-down nMOS Network
Current
Current
5V=1
GND=0
GND
+5V
A
B
Z
0
1
1
1
A = 0, B = 0 Output is Vdd=1
0
0
Current
GND
+5V
A
B
Z
GND
+5V
A
B
Z
GND
+5V
A
B
Z

## Slide 18: CMOS AND Gate
Pull-down pMOS Network
Pull-up nMOS Network
Build an AND gate by mirroring a NAND gate.
Problem: nMOS is poor at transmitting 5V and pMOS is poor at transmitting GND
Pull-up pMOS Network
Pull-down nMOS Network
GND
+5V
A
B
GND
+5V
Z
Take a NAND gate…
and invert the output
Takes two more transistors, but works! This is the reason that NANDs/NORs are faster than ANDs/ORs
GND
A
B
Z
+5V

## Slide 19: Logic Chips
HD74LS04P
1
2
3
4
5
6
7
8
9
10
11
12
13
14
HD74LS04P
Actual circuit is on a small chip of silicon
Package – Made of plastic or ceramic
Pins are connected to chip with internal wires
Pin number one is identified with a dot or notch
Pins are numbered in a counter-clockwise fashion
Standard chips use either TTL (Transistor-Transitor Logic), or CMOS transistors